## Slide 1: DRS – Team 4
Quality Function Deployment

## Slide 2: QFD - Customer Requirements
Fast response :
The speed at which the DRS responds to the pilot command is a prioritary requirement to take advantage of all the DRS zone in order to maximize the effectiveness of overtak while ensuring the driver’s safety.
Low actuation force:
Another key requirement is the magnitude of the actuation force which should be as little as possible in order to minimize the power consumption of the car.
Allow only 1 degree of freedom:
Since the actuator controls only one degree of freedom, the mechanism should comply with thisrequirement as well; therefore any deviation from the ideal movement should be minimal.
Minimum drag resistance:
The air flow aroun the DRS and the rear main wing are important to maximize performance and reduce non-ideal disturbing flows.

## Slide 3: QFD - Customer Requirements
Avoid residual oscillations:
The DRS should ideally stop exactly in the final position without ascillating about it; this means that spurious displacements need to be kept as little as possible and the time taken by the system to stabilize in the final position should be minimal.
Reliable and safe:
This requirement states a boundary (from regulations) on movement range, speed and accelerations.
Easy to assemble:
It might be needed a fast replacement of parts during races.
Lightweight
A light system is easier to actuate and is less burdensome on the car.

## Slide 4: QFD – Engineering Specifications
Opening time
The opening time determines how quick the DRS opens and therefore how much it can be exploited
Number of actuators:
Using multiple actuators (on MULTIPLE MECHANISMS) may help the drag reduction (e.g. exploit the main wing supports) of the actuators.
Actuating power:
The power needed to move the DRS is stolen from the engine gearbox reducing it’s performance, therefore it should be minimal.
Actuator width :
A wider actuator generally means more drag force to be overcomed. It should be minimal as well.
Distance between actuator and flap grounded joint:
It determines the leverage of the mechanism and the disturbance on the air flow.

## Slide 5: QFD – Engineering Specifications
Overshoot:
The overshoot determines a spurious variation of performance of the system which needs to be as little as possible
Oscillation stabilizing time:
The speed at which the overshoot settles on the final position is important to evaluate the reliability of the DRS.
Opening angle limit:
The angle of the open configuration determines how the force acts on the DRS and therefore the magnitude of drag and downforce.
Number of mechanism components:
Time to repair:

## Slide 6: QFD – Engineering Specifications
Opening time
The opening time determines how quick the DRS opens and therefore how much it can be exploited
Number of actuators:
Using multiple actuators (on MULTIPLE MECHANISMS) may help the drag reduction (e.g. exploit the main wing supports) of the actuators.
Actuating power:
The power needed to move the DRS is stolen from the engine gearbox reducing it’s performance, therefore it should be minimal.
Actuator width :
A wider actuator generally means more drag force to be overcomed. It should be minimal as well.
Distance between actuator and flap grounded joint:
It determines the leverage of the mechanism and the disturbance on the air flow.

## Slide 7: QFD - Engineering Specifications
Opening time
The opening time determines how quick the DRS opens and therefore how much it can be exploited
Number of actuators:
Using multiple actuators (on MULTIPLE MECHANISMS) may help the drag reduction (e.g. exploit the main wing supports) of the actuators.
Actuating power:
The power needed to move the DRS is stolen from the engine gearbox reducing it’s performance, therefore it should be minimal.
Actuator width :
A wider actuator generally means more drag force to be overcomed. It should be minimal as well.
Distance between actuator and flap grounded joint:
It determines the leverage of the mechanism and the disturbance on the air flow.

## Slide 8: QFD - Target values
Asd
Asd
Asd
Asd
Asd
Asd
asd

## Slide 9: QFD – «Hows»
Asd
Asd
Asd
Asd
Asd
Asd
asd

## Slide 10: QFD – Concept Generation
Asd
Asd
Asd
Asd
Asd
Asd
asd